## Slide 1
Pocket SDR Signal IDs
Ver. 0.9 2024-01-05
Ver. 0.10 2024-01-12
Ver. 0.11 2024-01-25
Ver. 0.12 2024-03-31

## Slide 2: Pocket SDR Signal IDs (1/3)
GPS [1][2][3] | 1575.42 | L1C/A | Q | -158.5 | BPSK(1) | 1023 | 1.023 | 1 | - | 1 | LNAV | 50 | 50 | - |  | L1CA
 |  | L1P(Y)*1 | I | -161.5 | BPSK(10) | 1week | 10.23 | 1week | - | 1week | LNAV | 50 | 50 | - |  | -
 |  | L1M*3 | I | ? | BOC(10,5) | ? | 5.115 | ? | ? | ? | ? | ? | ? | ? | Block IIR-M~ | -
 |  | L1C-D | I | -163.0 | BOC(1,1) | 10230 | 1.023 | 10 | - | 10 | CNAV-2 | 100 | 50 | BCH,LDPC | GPS III~ | L1CD
 |  | L1C-P | I | -158.25 | TMBOC(6,1,4/33) | 10230 | 1.023 | 10 | 1800 | 18000 | - | - | - | - |  | L1CP
 | 1227.6 | L2C/A | Q | -164.5 | BPSK(1) | 1023 | 1.023 | 1 | - | 1 | LNAV | 50 | 50 | - | Block IIR-M~ | -
 |  | L2P(Y)*1 | I | -164.5/-161.5 | BPSK(10) | 1week | 10.23 | 1week | - | 1week | LNAV | 50 | 50 | - |  | -
 |  | L2M*3 | I | ? | BOC(10,5) | ? | 5.115 | ? | ? | ? | ? | ? | ? | ? | Block IIR-M~ | -
 |  | L2C-M | Q/I | -160.0/ -158.5 | BPSK(1)+TDM | 10230 | 0.5115 | 20 | - | 20 | LNAV | 50 | 50 | - | Block IIR-M~ | -
 |  |  |  |  |  |  |  |  |  |  | CNAV | 50 | 25 | 1/2 |  | L2CM
 |  | L2C-L |  |  | BPSK(1)+TDM | 767250 | 0.5115 | 1500 | - | 1500 | - | - | - | - |  | -
 | 1176.45 | L5-I | I | -157.9/-157.0 | BPSK(10) | 10230 | 10.23 | 1 | 10 (NH) | 10 | CNAV | 100 | 50 | 1/2 | Block IIF~ | L5I
 |  | L5-Q | Q | -157.9/-157.0 | BPSK(10) | 10230 | 10.23 | 1 | 20 (NH) | 20 | - | - | - | - |  | L5Q
GLONASS [4][5][6][7] | 1602.0 + 0.5625K*2 | L1C/A*** | I | -161.0 | BPSK(0.5) | 511 | 0.511 | 1 | - / 2** | 1 / 2** | GLO-STR | 100 | 50 | - |  | G1CA
 |  | L1P | Q | ? | BPSK(5) | 5110000 | 5.11 | 1000 | - | 1000 | ? | ? | ? | - |  | -
 | 1600.995 | L1OCd | Q | ? | BPSK(1)+TDM | 1023 | 0.5115 | 2 | 2 (MC) | 4 | GLO-STR | 250 | 125 | 1/2 | GLO-K2~ | G1OCD
 |  | L1OCp |  |  | BOC(1,1)+TDM | 4092 | 0.5115 | 8 | - | 8 | - | - | - | - |  | G1OCP
 |  | L1SC *4 | I | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? |  | -
 | 1246.0 + 0.4375K*2 | L2C/A*** | I | -167.0 | BPSK(0.5) | 511 | 0.511 | 1 | - / 2** | 1 / 2** | GLO-STR | 100 | 50 | - |  | G2CA
 |  | L2P | Q | ? | BPSK(5) | 5110000 | 5.11 | 1000 | - | 1000 | ? | ? | ? | - |  | -
 | 1248.06 | L2CSI | Q | ? | BPSK(1)+TDM | ? | 0.5115 | ? | ? | ? | ? | ? | ? | ? | GLO-K2~ | -
 |  | L2OCp |  |  | BOC(1,1)+TDM | 10230 | 0.5115 | 20 | 50 | 1000 | - | - | - | - |  | G2OCP
 |  | L2SC *4 | I | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? | ? |  | -
 | 1202.025 | L3OCd | I | ? | BPSK(10) | 10230 | 10.23 | 1 | 5 (BC) | 5 | GLO-STR | 200 | 100 | 1/2 | GLO-K1~ | G3OCD
 |  | L3OCp | Q | ? | BPSK(10) | 10230 | 10.23 | 1 | 10 (NH) | 10 | - | - | - | - |  | G3OCP
Galileo[8] | 1575.42 | E1-A | Q | ? | BOC(15,2.5) | ? | 2.5575 | ? | ? | ? | G/NAV | ? | ? | ? | PRS | -
 |  | E1-B | I | -157.0 | CBOC(6,1,1/11) | 4092 | 1.023 | 4 | - | 4 | I/NAV | 250 | 125 | 1/2 | OS, SoL, CS | E1B
 |  | E1-C | I |  | CBOC(6,1,1/11) | 4092 | 1.023 | 4 | 25 | 100 | - | - | - | - |  | E1C
 | 1176.45 | E5a-I | I | -155.0 | BPSK(10) | 10230 | 10.23 | 1 | 20 | 20 | F/NAV | 50 | 25 | 1/2 | OS, CS | E5AI
 |  | E5a-Q | Q |  | BPSK(10) | 10230 | 10.23 | 1 | 100 | 100 | - | - | - | - |  | E5AQ
 | 1207.14 | E5b-I | I | -155.0 | BPSK(10) | 10230 | 10.23 | 1 | 4 | 4 | I/NAV | 250 | 125 | 1/2 | OS, SoL, CS | E5BI
 |  | E5b-Q | Q |  | BPSK(10) | 10230 | 10.23 | 1 | 100 | 100 | - | - | - | - |  | E5BQ
*1 AS ON, *2 K = {-7 ... +6}, *3 Military Signal, *4 Secured Service Signal, ** Odd FCN, *** (L1OF), (L2OF)
System | Carrier Freq. (MHz) | Signal | I/Q | Min Rec. Power (dBW) | Modulation | Primary Code |  |  | Overlay Code |  | Navigation Data |  |  |  | Notes | Pocket SDR Signal ID
 |  |  |  |  |  | Length (chip) | Chip Rate (Mcps) | Cycle (ms) | Length (chip) | Cycle (ms) | Data | Symbol Rate (sps) | Data Rate (bps) | FEC |  | 

## Slide 3: Pocket SDR Signal IDs (2/3)
Galileo (Cont.) | 1191.795 | E5a+b*5 | - | (-152.0) | 8-PSK(10) | 10230 | 10.23 | 1 | 100 | 100 | - | - | - | - |  | -
 | 1278.75 | E6-A | Q | ? | BOC(10,5) | ? | 5.115 | ? | ? | ? | G/NAV | ? | ? | ? | PRS | -
 |  | E6-B | I | -155.0 | BPSK(5) | 5115 | 5.115 | 1 | - | 1 | C/NAV | 1000 | 500 | 1/2 | CAS, HAS | E6B
 |  | E6-C | I |  | BPSK(5) | 5115 | 5.115 | 1 | 100 | 100 | - | - | - | - |  | E6C
QZSS [9][10][11][12] | 1575.42 | L1C/A | I/Q | -158.5*6 | BPSK(1) | 1023 | 1.023 | 1 | - | 1 | LNAV | 50 | 50 | - |  | L1CA
 |  | L1C/B | I | -158.5 | BOC(1,1) | 1023 | 1.023 | 1 | - | 1 | LNAV | 50 | 50 | - |  | L1CB
 |  | L1C-D | I | -163.0*7 | BOC(1,1) | 10230 | 1.023 | 10 | - | 10 | CNAV2 | 100 | 50 | BCH,LDPC |  | L1CD
 |  | L1C-P | Q | -158.25 | BOC(1,1) | 10230 | 1.023 | 10 | 1800 | 18000 | - | - | - | - | Block I | L1CP
 |  |  | I | -158.25*8 | TMBOC(6,1,4/33) | 10230 | 1.023 | 10 | 1800 | 18000 | - | - | - | - | Block II | L1CP
 |  | L1S | I | -161.0/-158.5 | BPSK(1) | 1023 | 1.023 | 1 | - | 1 | L1S | 500 | 250 | 1/2 | SLAS | L1S
 | 1227.6 | L2C-M | I | -160.0/ -158.5 | BPSK(1)+TDM | 10230 | 0.5115 | 20 | - | 20 | CNAV | 50 | 25 | 1/2 |  | L2CM
 |  | L2C-L |  |  | BPSK(1)+TDM | 767250 | 0.5115 | 1500 | - | 1500 | - | - | - | - |  | -
 | 1176.45 | L5-I | I | -157.9/-157.0 | BPSK(10) | 10230 | 10.23 | 1 | 10 (NH) | 10 | CNAV | 100 | 50 | 1/2 |  | L5I
 |  | L5-Q | Q | -157.9/-157.0 | BPSK(10) | 10230 | 10.23 | 1 | 20 (NH) | 20 | - | - | - | - |  | L5Q
 |  | L5S-I | I | -157.0*9 | BPSK(10) | 10230 | 10.23 | 1 | - | 1 | L5S | 500 | 250 | 1/2 | Normal mode | L5SI
 |  |  |  |  |  |  |  |  | 2 (MC) | 2 | L5S | 500 | 250 | 1/2 | Verif. mode | L5SIV
 |  | L5S-Q | Q |  | BPSK(10) | 10230 | 10.23 | 1 | 20 (NH) | 20 | - | - | - | - | Normal mode | L5SQ
 |  |  |  |  |  |  |  |  | 2 (MC) | 2 | - | - | - | - | Verif. mode | L5SQV
 | 1278.75 | L6D | I | -155.7 | BPSK(5)+TDM | 10230 | 2.5575 | 4 | - | 4 | L6D | 2000 | 2000 | RS | CLAS | L6D
 |  | L6L |  |  | BPSK(5)+TDM | 1048575 | 2.5575 | 410 | 2 (MC) | 820 | - | - | - | - | Block I | -
 |  | L6E |  |  | BPSK(5)+TDM | 10230 | 2.5575 | 4 | - | 4 | L6E | 2000 | 2000 | RS | MADOCA-PPP | L6E
BeiDou [13][14][15] [16][17] | 1561.098 | B1I | I | -163.0 | BPSK(2) | 2046 | 2.046 | 1 | 20 (NH) | 20 | D1 | 50 | 50 | BCH |  | B1I
 |  |  |  |  |  |  |  | 1 | - | 1 | D2 | 500 | 500 | BCH | GEO | B1I
 |  | B1Q*10 | Q | ? | BPSK(2) | ? | 2.046 | ? | ? | ? | ? | ? | ? | ? |  | -
 | 1575.42 | B1C-D | I | -159.0/ -161.0 | BOC(1,1) | 10230 | 1.023 | 10 | - | 10 | B-CNAV1 | 100 | 50 | NB-LDPC | BDS-3 | B1CD
 |  | B1C-P | I |  | QMBOC(6,1,4/33) | 10230 | 1.023 | 10 | 1800 | 18000 | - | - | - | - |  | B1CP
 |  | B1A-D*10 | Q | ? | BOC(14,2) | ? | 2.046 | ? | ? | ? | ? | ? | ? | ? |  | -
 |  | B1A-P*10 | Q |  |  | ? | 2.046 | ? | ? | ? | - | - | - | - |  | -
 | 1176.45 | B2a-D | I | -156.0/ -158.0 | BPSK(10) | 10230 | 10.23 | 1 | 5 | 5 | B-CNAV2 | 50 | 25 | NB-LDPC | BDS-3 | B2AD
 |  | B2a-P | Q |  | BPSK(10) | 10230 | 10.23 | 1 | 100 | 100 | - | - | - | - |  | B2AP
 | 1207.14 | B2I | I | ? | BPSK(2) | 2046 | 2.046 | 1 | 20 (NH) | 20 | D1 | 50 | 50 | BCH |  | B2I
 |  |  |  |  |  |  |  | 1 | - | 1 | D2 | 500 | 500 | BCH | GEO | B2I
*5 AltBOC *6 -164.0 dBW (SVID=7), *7 -167.2 dBW (SVID=7), *8 -162.4 dBW (SVID=7), *9 -162.6 dBW (SVID=3), *10 Authorized signal
System | Carrier Freq. (MHz) | Signal | I/Q | Min Rec. Power (dBW) | Modulation | Primary Code |  |  | Overlay Code |  | Navigation Data |  |  |  | Notes | Pocket SDR Signal ID
 |  |  |  |  |  | Length (chip) | Chip Rate (Mcps) | Cycle (ms) | Length (chip) | Cycle (ms) | Data | Symbol Rate (sps) | Data Rate (bps) | FEC |  | 

## Slide 4: Pocket SDR Signal IDs (3/3)
BeiDou (Cont.) | 1207.14 | B2Q*10 | Q | ? | BPSK(10) | 10230 | 10.23 | 1 | ? | ? | ? | ? | ? | ? |  | -
 | 1207.14 | B2b-I | I | -160.0/ -162.0 | BPSK(10) | 10230 | 10.23 | 1 | - | 1 | B-CNAV3 | 1000 | 500 | NB-LDPC | BDS-3 | B2BI
 |  |  |  |  |  |  |  |  |  |  | B2b-PPP | 1000 | 500 | NB-LDPC | BDS-3, GEO | B2BI
 |  | B2b-Q*10 | Q | ? | BPSK(10) | 10230 | 10.23 | 1 | ? | ? | ? | ? | ? | ? | BDS-3 | -
 | 1191.795 | B2a+b*11 | - | ? | 8-PSK(10) | 10230 | 10.23 | 1 | ? | ? | - | - | - | - |  | -
 | 1268.52 | B3I | I | -163.0 | BPSK(10) | 10230 | 10.23 | 1 | 20 (NH) | 20 | D1 | 50 | 50 | BCH |  | B3I
 |  |  |  |  |  |  |  | 1 | - | 1 | D2 | 500 | 500 | BCH | GEO | B3I
 |  | B3Q*10 | Q | ? | BPSK(10) | ? | 10.23 | ? | ? | ? | ? | ? | ? | ? |  | -
 |  | B3A-D*10 | I | ? | BPSK(10) | ? | 10.23 | ? | ? | ? | ? | ? | ? | ? | BDS-3 | -
 |  | B3A-P*10 | I |  | BPSK(10) | ? | 10.23 | ? | ? | ? | - | - | - | - |  | -
NavIC [18][19] | 1575.42 | L1-SPS-D | Q | -159.6 | BOC(1,1) | 10230 | 1.023 | 10 | - | 10 | IRN-NAV | 100 | 50 | BCH,LDPC | NVS-01~ | I1SD
 |  | L1-SPS-P | I | -158.2 | CSBOC(6,1,4/33) | 10230 | 1.023 | 10 | 1800 | 18000 | - | - | - | - |  | I1SP
NavIC [18][19] | 1176.45 | L5-SPS | *12 | -159.0 | BPSK(1) | 1023 | 1.023 | 1 | - | 1 | IRN-NAV | 50 | 25 | 1/2 |  | I5S
 |  | L5-RS-D | *12 | ? | BOC(5,2) | ? | 2.046 | ? | ? | ? | ? | 50 | 25 | 1/2 | *10 | -
 |  | L5-RS-P | *12 | ? | BOC(5,2) | ? | 2.046 | ? | ? | ? | - | - | - | - | *10 | -
 | 2492.028 | S-SPS | *12 | -162.3 | BPSK(1) | 1023 | 1.023 | 1 | - | 1 | IRN-NAV | 50 | 25 | 1/2 |  | ISS
 |  | S-RS-D | *12 | ? | BOC(5,2) | ? | 2.046 | ? | ? | ? | ? | 50 | 25 | 1/2 | *10 | -
 |  | S-RS-P | *12 | ? | BOC(5,2) | ? | 2.046 | ? | ? | ? | - | - | - | - | *10 | -
SBAS | 1575.42 | L1C/A | I | - | BPSK(1) | 1023 | 1.023 | 1 | - | 1 | SBAS | 500 | 250 | 1/2 | PRN120-158 | L1CA
 | 1176.45 | L5-I | I | - | BPSK(10) | 10230 | 10.23 | 1 | 2 (MC) | 2 | L5 SBAS | 500 | 250 | 1/2 | PRN120-158 | L5I
 |  | L5-Q | Q | - | BPSK(10) | 10230 | 10.23 | 1 | 2 (MC) | 2 | - | - | - | - |  | L5Q
[1] IS-GPS-200K, Navstar GPS space segment/navigation user interfaces - interface specification, 2019, [2] IS-GPS-800F, Navstar GPS space segment/user segment L1C interface - interface specification, 2019, [3] IS-GPS-705A, Navstar GPS space segment/user segment L5 interface - interface specification, 2010, [4] GLONASS interface control document - navigation radiosignal in bands L1, L2, version 5.1, 2008, [5] GLONASS interface control document - code division multiple access open service navigation signal in L1 frequency band, edition 1.0, 2016, [6] GLONASS interface control document - code division multiple access open service navigation signal in L2 frequency band, edition 1.0, 2016, [7] GLONASS interface control document - code division multiple access open service navigation signal in L3 frequency band, edition 1.0, 2016, [8] European GNSS (Galileo) open service signal-in-space interface control document (OS SIS ICD), Issue 1, Revision 3, 2016, [9] Quasi-Zenith satellite system interface specification - satellite positioning, navigation and timing service (IS-QZSS-PNT-003), 2018, [10] Quasi-zenith satellite system interface specification - sub-meter level augmentation service (IS-QZSS-L1S-003), 2018, [11] Quasi-zenith satellite system interface specification - centimeter level augmentation service (IS-QZSS-L6-003), 2018, [12] Quasi-zenith satellite system interface specification - positioning technology verification service (IS-QZSS-TV-004), 2023, [13] BeiDou navigation satellite system signal in space interface control document - open service signal B1I, version 3, 2019, [14] BeiDou navigation satellite system signal in space interface control document - open service signal B1C, version 1.0, 2017, [15] BeiDou navigation satellite system signal in space interface control document - open service signal B2a, version 1.0, 2017, [16] BeiDou navigation satellite system signal in space interface control document - open service signal B3I, version 1.0, 2018, [17] BeiDou navigation satellite system signal in space interface control document - Precise Point Positioning service signal PPP-B2b, version 1.0, 2020, [18] Indian Regional Navigation Satellite System, Signal in space ICD for standard positioning service version 1.1, 2017, [19] NAVIC signal in space ICD for standard positioning service in L1 frequency version 1.0, 2023
*10 Authorized signal, *11 ACE-BOC, *12 Interplex Modulation
System | Carrier Freq. (MHz) | Signal | I/Q | Min Rec. Power (dBW) | Modulation | Primary Code |  |  | Overlay Code |  | Navigation Data |  |  |  | Notes | Pocket SDR Signal ID
 |  |  |  |  |  | Length (chip) | Chip Rate (Mcps) | Cycle (ms) | Length (chip) | Cycle (ms) | Data | Symbol Rate (sps) | Data Rate (bps) | FEC |  | 

## Slide 5: GNSS Signal Band
1160
1170
1180
1190
1200
1210
1220
1230
1240
1250
1260
1270
1280
1290
(MHz)
1510
1520
1530
1540
1500
1560
1570
1580
1590
1600
1610
1620
1630
1640
L1 Band
L2/L5/L6 Band
1575.42
L1P(Y)
L1C/A
L1C
1227.6
L2P(Y)
L2C
1176.45
1278.75
L5
E6
L6
L2C
E5a
1207.14
E5b
E1-B,C
L1C/A, L1S
L1C/B, L1C
1602.0
1246.0
L2C/A, L2OC
L5, L5S
1561.098
B1I
B1C
B2a
B2I
B2b
1268.52
B3I
L1-SPS
L5-SPS
L1C/A
L5
(MHz)
GPS
GLONASS
Galileo
QZSS
NavIC
SBAS
BeiDou
L3OC
L1C/A,
L1OC